## Slide 1
Suk-Ju Kang, Sogang University
Considerations for Standardization of VR Display

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3
Considerations for Standardization of VR Display |  |  | 
Date: 2017-07-10 |  |  | 
Author(s): Suk-Ju Kang |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Suk-Ju Kang | Sogang University | +82-10-7103-6520 | sjkang@sogang.ac.kr
IEEE P3333.3 HMD Based 3D Content Motion Sickness Reducing Technology
[Dong Il Seo and dillon@volercreative.com]

## Slide 4: Outline
Introduction
Considerations in VR Displays
  Part I: Display Resolution
  Part II: Chromatic Aberration and Correction
  Part III: Display Technology Trend in VR
Conclusion

## Slide 5: Introduction
Challenge of Virtual Reality
  Users feel gaps on their sense between the reality and virtual reality because of a motion-to-photon latency
  This causes dizziness and motion sickness to user
Motion-to-photon latency must be measured and compensated!
Problems from latency of HMD
Motion sickness
Dizziness
Human perception
Blurring
Image judder

## Slide 6: Introduction
Motion-to-Photon Latency
  Motion-to-Photon latency is the time needed for a user movement to be fully reflected on a display screen
  Low motion-to-photon (< 20 ms) latency is a prerequisite to convince user’s mind that user is in another place
  A high motion-to-photon latency makes a poor virtual reality experience
Tracker
CPU
GPU
Display
Photons
Optics
Head motion
User’s retina
Under 20 milliseconds of latency for comfortability

## Slide 7: Introduction
We have to consider several factors in VR displays
  Display Resolution
  Chromatic Aberration and Correction

## Slide 8: Part i: Display Resolution
Considerations In VR Displays

## Slide 9: Display Resolution
Chromatic Aberration
  General HW structure in HMDs
    Display panel
    Fisheye lens
    Perceptional image
Fisheye lens

## Slide 10: Display Resolution
Pixels per inch (PPI)
  Measurement of the pixel density (resolution) of an electronic image device such as a monitor or television display
  A 100×100 pixel image printed in a 1 inch square has a resolution of 100 pixels per inch

## Slide 11: Display Resolution
JDI
  New displays will be 3.42-inch low temperature polysilicon (LTPS) TFT LCD specifically designed for virtual reality (VR) head mount displays

## Slide 12: Display Resolution

## Slide 13: Display Resolution
Samsung
  A new display targeting use in VR headsets packs 2,024 x 2,200 pixels into a 3.5″ form-factor, delivering an impressive 858 PPI (Nearly twice the 460 PPI of the Rift and the Vive)
  The display is also capable of a 90Hz refresh rate and 100 nits brightness
Previous VR display
New VR display

## Slide 14: Part iI: Chromatic Aberration and Correction
Considerations In VR Displays

## Slide 15: Chromatic Aberration and Correction
Chromatic Aberration
  Fisheye lens
    The Fisheye lens gives users a wide viewing angle
    Normal HMDs provide a FOV(Field Of View) of over 110°
    Lens has a large refractive index

## Slide 16: Chromatic Aberration and Correction
Chromatic Aberration
  Reason for chromatic aberration
    The separation of light is called chromatic aberration because of different refractive indexes depending on the wavelength of light

## Slide 17: Chromatic Aberration and Correction
Correction
  Fisheye lens modeling
    Modeling is required for the precise pre-distortion
  Measurement method
    (a): Measuring HMD images with wide angle lens camera
    (b): Camera calibration with the chess board
    (c): Photographed VR images
(a)
(b)
(c)

## Slide 18: Chromatic Aberration and Correction
Correction
  Measurement method
    Parameter extraction through camera calibration
    (a):Photos taken by using the chess board in virtual space
    (b):Optimal parameter extraction using multiple photographs
(a)
(b)

## Slide 19: Chromatic Aberration and Correction
Correction
  Calibration result
    (a): Original image
    (b): Image with the pre-distortion
    (c): User's perceptional image
(a)
(b)
(c)

## Slide 20: Part iII: Display Technology Trend in VR
Considerations In VR Displays

## Slide 21: Display Technology Trend in VR
2017 Display Week

## Slide 22: Display Technology Trend in VR
Samsung
  HMD panel
  High PPI panel

## Slide 23: Display Technology Trend in VR
Samsung
  High speed
  HDR panel (Peak Brightness = 1000 nit)

## Slide 24: Display Technology Trend in VR
LG
  HDR
  Curved
  8K / UHD

## Slide 25: Display Technology Trend in VR
BOE
  1900 PPI panel
  8K Picture
  Foldable

## Slide 26: Display Technology Trend in VR
Japan display
  Aerial display
  Fast response panel

## Slide 27: Display Technology Trend in VR
3M
  Screen-door-effect reduction in virtual reality headsets

## Slide 28: Display Technology Trend in VR
Display measurement system
  Near-eye display measurement

## Slide 29: Display Technology Trend in VR
Display measurement system
  Near-eye display measurement

## Slide 30: Display Technology Trend in VR
Display measurement system
  Perceptual resolution measurement

## Slide 31: Conclusion
We have to measure and reduce the motion-to-photon latency
  The latency measurement system is required for quantitative numerical calculations
  Finally, the latency compensation technique is required to reduce the motion sickness
Considerations in Displays
  We have to use the high PPI display, but consider HW resources to render the output image
  In order to reduce the chromatic aberration, we have to use the pre-correction technique