## Slide 1
Minseok OH, Namgi KIM
Kyonggi University
Transmission Technologies and Requirements for Wireless VR

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3
Technical Requirements for VR |  |  | 
Date: 2017-10-31 |  |  | 
Author(s): |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Minseok OH | Kyonggi University |  | msoh@kgu.ac.kr
Namgi KIM | Kyonggi University |  | ngkim@kgu.ac.kr
IEEE P3079 HMD Based 3D Content Motion Sickness Reducing Technology
[Dongil Seo, Dillon@volercreative.com]

## Slide 4: Abstract
Technical capabilities of a transmission technology provides what the technology can offer when it is applied
IEEE 802.11ay [1] [2], IMT Vision (IMT–2020 and beyond) [3]
Some standard organizations have described requirements to provide a high quality VR service to users
IEEE 802.11ay [4], MPEG m39532 [5], IEEE 802.21 [6]
We present the discrepancies between technical requirements for HMD and the technical capabilities for wireless HMD transmission technology candidates

## Slide 5: Capabilities of IEEE 802.11ay
Based on IEEE 802.11ay PAR [1] and Functional Requirements document [2]
Maximum throughput
At least 20 Gbps, as measured at the MAC data service access point (SAP)
Coexistence
Support backward compatibility with legacy directional multigigabit (DMG) devices (IEEE 802.11ad) operating in the same band
Support coexistence with legacy devices operating in the same band

## Slide 6: Capabilities of IEEE 802.11ay – cont’d
Range
At least 10 meters in an indoor environment
At least 100 meters in an outdoor environment
Power Efficiency
At least the same power efficiency per STA as legacy DMG devices (11ad).
Note that 802.11ad does not assert any power consumption requirements. [3]

## Slide 7: Capabilities of IEEE 802.11ay – cont’d
Video Requirements
Support lightly compressed 4K and 8K UHD video for data rate, packet loss rate, delay measured at MAC SAP
Parameter | Value | Description
Data rate | 1.5 Gbps (Peak) | 4K UHD 2160p (RGB): 3840x2160 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color
Packet loss rate | 10-8 | 
Delay | 10 ms | 
Parameter | Value | Description
Data rate | 8.0 Gbps (Peak) | 8K UHD 4320p (RGB): 7680x4320 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color
Packet loss rate | 10-8 | 
Delay | 10 ms | 

## Slide 8: Capabilities of IEEE 802.11ay – cont’d
Video Requirements
Support uncompressed 4K and 8K UHD video for data rate, packet loss rate, delay measured at MAC SAP
Parameter | Value | Description
Data rate | 18.0 Gbps | 4K UHD uncompressed 3840x2160 pixels, 30 bits/pixels, 60 frames/s, 8 bit per color. Chroma subsampling (4:4:4)
Packet loss rate | 10-8 | 
Delay | 10 ms | 
Parameter | Value | Description
Data rate | 28.0 Gbps | 8K UHD uncompressed 7680x4320 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color. Chroma subsampling (4:2:0)
Packet loss rate | 10-8 | 
Delay | 10 ms | 

## Slide 9: Capabilities of IEEE 802.11ay – cont’d
Fast Link Setup
Provides a means of providing secure fast link setup
Outdoor Support
Provides a means of supporting outdoor operations
Mobility Support
Provides mobility operations at a pedestrian speed (e.g., 3 km/h) or body movements (i.e., neck roll, neck pitch, neck yaw)

## Slide 10: Capabilities of IMT-2020
Based on ITU-R M.2083-0, IMT-2020 and beyond [3]
(Framework and overall objectives of the future development of IMT for 2020 and beyond)

## Slide 11: Capabilities of IMT-2020 – cont’d

## Slide 12: Capabilities of IMT-2020 – cont’d
Key capabilities | Descriptions | Values
Peak data rate | Maximum achievable data rate under ideal conditions per user/device (in Gbps) | 20 Gbps
User experienced data rate | Achievable data rate that is available ubiquitously across the coverage area to a mobile user/device (in Mbit/s or Gbit/s). | 100 Mbps
Latency | The contribution by the radio network to the time from when the source sends a packet to when the destination receives it (in ms). | 1 ms
Mobility | Maximum speed at which a defined QoS and seamless transfer between radio nodes which may belong to different layers and/or radio access technologies (multi-layer/-RAT) can be achieved (in km/h). | 500 km/h

## Slide 13: Capabilities of IMT-2020 – cont’d
Key capabilities | Descriptions | Values
Energy efficiency | Energy efficiency has two aspects: – on the network side, energy efficiency refers to the quantity of information bits transmitted to/ received from users, per unit of energy consumption of the radio access network (RAN) (in bit/Joule); – on the device side, energy efficiency refers to quantity of information bits per unit of energy consumption of the communication module (in bit/Joule). | 100 times more efficient than IMT-advanced
Spectrum efficiency | Average data throughput per unit of spectrum resource and per cell (bit/s/Hz) | 3 times more efficient than IMT-advanced
Area traffic capacity | Total traffic throughput served per geographic area (in Mbit/s/m2). | 10 Mbits/m2

## Slide 14: Functional Requirements of 802.11ay
IEEE 802.11ay usage scenarios provides key functional requirements for AR/VR [3]
 | Requirements | Notes
Data rate | ~20 Gbps | 
Latency | < 5 ms | 
Jitter | < 5 ms | 
PER (packet error rate) | 10-2 | 
Distance | 5 m (indoor) | 
Video Quality | 3D 4K | HDMI 2.0
Range of Motion for head-worn wearable | Neck Roll | 0.17 (s/60deg)
 | Neck Pitch | 0.14 (s/60deg)
 | Neck Yaw | 0.13 (s/60deg)
Device mobility | Pedestrian speeds | < 4 km/hr

## Slide 15: Quality Requirements for VR of MPEG
Based on MPEG m39532 (October 2016) [4]
Defines quality requirements for high quality VR services
Requirement 1 (video), Resolution:
40 pixels/degree or 12K (11520 x 6480)
Requirement 2 (video), Frame rate:
90 fps
Requirement 3 (video), Stitching errors
Rendering processes shall not introduce additional stitching errors
Requirement 4 (audio), 3D Audio:
Support of scene-based and/or environment audio

## Slide 16: Quality Requirements for VR – cont’d
Requirement 5 (immersion), Motion-to-photon and motion-to-audio latency:
Maximum 20 ms
Requirement 6 (immersion), Foreground & parallax:
Objects in the foreground shall be far enough to prevent nausea
Interactive parallax with background shall be present for such objects

## Slide 17: Handover Requirements for VR [6]
Handover from a high-speed network to a low-speed network should not degrade severely the VR contents delivery service quality
The result can be devastating especially when destroying the portion containing the important information about the VR contents

## Slide 18: Checking Facts
Discrepancies between HMD requirements and what the candidate technologies can offer
 | HMD Requirements |  |  | Capabilities | 
 | 802.11ay | MPEG | 802.21 | 802.1ay | IMT-2020
Data rate | ~ 20 Gbps | n/a | n/a | <= 20 Gbps | <= 20 Gbps (user-experienced data rate <= 100 Mbps)
Latency | 5 ms (motion-to-photon) | <= 20 ms (motion-to-audio latency as well) | n/a | 5 or 10 ms | 1 ms
Jitter | < 5 ms | n/a | n/a | n/a | n/a
PER (packet error rate) | 10-2 | n/a | n/a | ~ 10-8 | n/a
Distance | 5 m | n/a | n/a | >= 10 m indoor, >= 100 m outdoor | n/a
Resolution | 3D 4K (2 x 3840x2160) | 12K (11520 x 6480) | n/a | Not applicable | Not applicable

## Slide 19: Checking Facts – cont’d
 |  | VR Requirements |  |  | Capabilities | 
 |  | 802.11ay | MPEG | 802.21 | 802.1ay | IMT-2020
Range of Motion for head-worn wearable | Neck Roll | 0.17 (s/60deg) | n/a | n/a | n/a | n/a
 | Neck Pitch | 0.14(s/60deg) | n/a | n/a | n/a | n/a
 | Neck Yaw | 0.13 (s/60deg) | n/a | n/a | n/a | n/a
Device mobility |  | Pedestrian speeds < 4 km/h | n/a | n/a | n/a | 500 km/h
Frame rate |  | n/a | 90 fps | n/a | Not applicable | Not applicable

## Slide 20: Checking Facts – cont’d
 | VR Requirements |  |  | Capabilities | 
 | 802.11ay | MPEG | 802.21 | 802.1ay | IMT-2020
Stitching errors | n/a | Rendering processes shall not introduce additional stitching errors | n/a | Not applicable | Not applicable
3D Audio | n/a | Support of scene-based and/or environment audio | n/a | Not applicable | Not applicable
Foreground & parallax | n/a | Objects in the foreground shall be far enough to prevent nausea and interactive parallax with background shall be present for such objects | n/a | Not applicable | Not applicable
Network handover | n/a | n/a | Handover from a high-speed network to a low-speed network should not degrade severely the VR contents delivery service quality | n/a | n/a

## Slide 21: Conclusion
We need a list of new requirements to reduce HMD Based 3D content motion sickness
We need to cooperate with motion-sickness experts in diverse fields such as medical, psychological, video/audio, and network areas
Bring those to the related standard organization so that the requirements can be merged into their standard

## Slide 22: References
[1] https://mentor.ieee.org/802.11/dcn/14/11-14-1151-08-ng60-ng60-proposed-par.docx
[2] https://mentor.ieee.org/802.11/dcn/15/11-15-1074-00-00ay-11ay-functional-requirements.docx
[3] Recommendation ITU-R M.2083-0, IMT Vision – Framework and overall objectives of the future development of IMT for 2020 and beyond
[4] https://mentor.ieee.org/802.11/dcn/15/11-15-0625-04-00ay-ieee-802-11-tgay-usage-scenarios.pptx
[5] ISO/IEC JTC1/SC29/WG11 MPEG 116/m39532, Oct. 2016
[6] https://mentor.ieee.org/802.21/dcn/16/21-16-0097-00-0000-mih-for-vr-content-based-hmd.docx
[7] https://mentor.ieee.org/802.11/dcn/09/11-09-0228-05-00ad-functional-requirements.doc