## Slide 1
Suk-Ju Kang, Sogang University
Motion Blur Measurement System for VR Head Mounted Displays

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3
Motion Blur Measurement System for VR Head Mounted Displays |  |  | 
Date: 2018-07-09 |  |  | 
Author(s): Suk-Ju Kang |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Suk-Ju Kang | Sogang University | +82-10-7103-6520 | sjkang@sogang.ac.kr
IEEE 3079 Cybersickness Reduction Working Group
[Dong Il Seo and dillon@volercreative.com]

## Slide 4: Outline
Introduction
Moving Picture Response Time (MPRT)
Motivation
Proposed Measurement System
Experimental Results
Summary

## Slide 5: Introduction
Head Mounted Display (HMD)
  HMD offers a high level of immersion, but several problems cause motion sickness
Main reasons of motion sickness
  Motion-to-photon latency – Seo et al. (2017)
    The time needed for a user movement to be fully reflected on a display screen
  Motion blur
    It greatly affects picture quality perceived by users
      Quantitative measurement is necessary

## Slide 6: Moving Picture Response Time (MPRT)
Perceptual characteristics of human
  Perceived motion blur is different from motion blur which simply appears in a moving picture
  A perceived image is a result from the temporally continuous image integration
    It reflects the eye tracking synchronized with the moving picture
MPRT is measured by the perceived image
  Edge which shows difference of luminance would be blurred
  Measure blurred edge by number of pixel

## Slide 7: Moving Picture Response Time (MPRT)
MPRT calculations

## Slide 8: Motivation
Conventional methods of measuring MPRT
  Tracking camera model : Camera(Eye) follows the object
  High-speed camera model : Camera is fixed to using eye trace integration
High-speed camera model (Target model)
  Easy to synchronize between camera frame per second (fps) and display fps
  Need additional eye trace integration process to measure BEW

## Slide 9: Motivation
Example demo of high-speed camera model (Non head-movement environment )
  Camera : Sony DSC-RX100 MK5 (960 fps high-speed camera)
  Measurement object (Displayed on 60 fps mobile panel)
    White box width: 100 pixels
    Scroll speed: 30 PPF (constant)
Test pattern captured by high-speed camera
Test pattern displayed on the mobile panel

## Slide 10: Proposed Measurement System
Head Movement-based Motion Blur Measurement System
Overall process of the proposed measurement system

## Slide 11: Proposed Measurement System
(1) Head movement simulation (rotary platform)
  VR test pattern generation
    Test pattern moves according to rotary platform movement with the rotation angle
    3D virtual space (spherical space) → 2D virtual space (plane space) projection
      To maintain width of the pattern(white object) constant respect to the view angle

## Slide 12: Proposed Measurement System
(2) Image acquisition
  During head movement simulation, test pattern on panel moves accordingly
  Simultaneously, images are captured by high-speed camera
    Remote controlling using IR receiver

## Slide 13: Proposed Measurement System
(3) Scroll velocity calculation
  Velocity of the test pattern has to be measured to calculate continuous
  Rotation angle() is extracted by encoder
    The angular velocity () is a value obtained by differentiating the rotation angle
    Angular velocity and scroll velocity are related
Relationship between scroll velocity and rotation angle

## Slide 14: Proposed Measurement System
(4) MPRT calculation
  Interface of MPRT calculation
Interface of MPRT calculation program

## Slide 15: Experimental Results
Encoder data
  Rotation angle data
    Total 241,664 samples
    Range of angle (pitch) : - 35.982 ~ 35.982

## Slide 16: Experimental Results
Scroll velocity & MPRT
  Angle (pitch) data – time
  Velocity (PPF)
    Scroll velocity is calculated by angle
Time – pitch graph
  Velocity – time
  MPRT (ms)
Time – velocity graph

## Slide 17: Experimental Results
MPRT results
  MPRT had similar values when the scroll velocity were different
  MPRT had smaller values when display frame rates were larger
MPRT according to scroll velocity
MPRT according to display frame rate

## Slide 18: Summary
We proposed Head Movement-based Motion Blur Measurement System for HMD
  MPRT metric is used to motion blur measurement and it is a conventional method
  The rotary platform controlled orientations of an HMD device by a motion generator
  The encoder collected angle data of physical rotation
The proposed system considered difference between HMD and existing display system
  The correlation between actual physical rotation and VR space was considered
  For HMD, scroll velocity of MPRT metric is not constant