## Slide 1
Brain Activity Changes by MTP Latency
[Lim, Hyun Kyoon, PhD
Korea Research Institute of Standards and Science]

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3: IEEE 3079.1 HMD Based VR Sickness Reducing Technology Seo, Dong Il Dillon, dillon.seo@dtcp.capital
Brain Activity Changes by MTP Latency |  |  | 
Date: 2021-04-19 |  |  | 
Author(s): Lim, Hyun Kyoon |  |  | 
Name | Affiliation | Phone | Email
Lim, Hyun Kyoon | KRISS |  | hlim@kriss.re.kr
Kwon, Moonyoung | KRISS |  | mykwon@kriss.re.kr
Jang, Kyoung-Mi | KRISS |  | km_jang@kriss.re.kr
Nam, Sun Gu | KAIST |  | naisz@kaist.ac.kr
Kim, Da Mee | KRISS |  | dameeing@kriss.re.kr

## Slide 4: Aim of Study
VR sickness from
  Rotation, speed of movement, field of view, display type, motion-to-photon (MTP) latency, age, experience, …
Previous study
  Evaluate VR sickness using subjective measurement such as simulator sickness questionnaire (SSQ), fast motion sickness scale (FMS) scores
Goal
1. Find objective indicator of VR sickness by MTP latency
2. Propose safety guideline of MTP latency

## Slide 5: Progress of the Study
Conduct experiment (ongoing)
  Goal: 30 subjects
  Performance : 15 subjects
EEG analysis (ongoing)
  Frequency power of 0 ms vs. 60 ms
Create VR(with MTP latency) Videos
Fix Experimental Procedure
Conduct Experiment with EEG
Analysis of EEG Changes by MTP Latency
VR Video Evaluation
Find Indicator and propose safety guideline of latency

## Slide 6: Experimental Design
Neck movement
  80°/sec
Beep sound
  Every second
  To limit movement speed
40°
Beep
Beep
40°

## Slide 7: Subjective Measurement: Misery Scale
Bos et al., 2005

## Slide 8: Objective Measurement: EEG
Device
  GSN-HydroCel 256-channel (EGI, www.egi.com)
Analysis
  Spectral density changes between ‘before’ and ‘after’ conditions
    Delta(1 – 4 Hz), theta (4 – 8 Hz), alpha (8 – 13 Hz), beta (13 – 30 Hz), gamma (30 – 50 Hz)

## Slide 9: Experimental Procedure
Additional latency
  0 ms (only device latency), 30 ms, 60 ms
2 trials/condition
Task: 60 s
After: 30 s
Before: 30 s

## Slide 10: Results – Subjective Measurement
1.46 ± 1.17
2.23 ± 1.42
*
13 subjects

## Slide 11: Results – Objective(EEG) Measurement
Delta (1 – 4 Hz)
only device latency
Before
After
Theta (4 – 8 Hz)
Gamma (30 – 50 Hz)
Alpha (8 – 13 Hz)
Beta (13 – 30 Hz)
Before
After
device latency + 60 ms
*
13 subjects

## Slide 12: Tentative Conclusion
VR sickness by MTP latency
  Delta, theta, alpha powers may be indicators
  Increase powers on most of regions
  Especially, delta power on frontal area
  Similar results with previous work (Lim et al., 2021)
Lim et al., 2021

## Slide 13: Future Work
Future Work
Current Steps
Create VR(with MTP latency) Videos
Fix Experimental Procedure
Conduct Experiment with EEG
Analysis of EEG Changes by MTP Latency
VR Video Evaluation
Find Indicator and propose safety guideline of latency

## Slide 14
Thank You